## Slide 1: Boolean Algebra
Slides by Rob Nash, Senior Lecturer
  With excerpts from Arnie Berger, Wooyoung Kim, Linda Null
Readings: See schedule
“The Analytical Engine weaves algebraically patterns just as the Jacquard Loom weaves flowers and leaves.” – Ada
“2x + 6x => 8x” //less symbols, more compact, reduced
Hardware Artifact: AND, OR, and NOT DIPPs
Circuit
Truth Table
Boolean Function
1
2
3

## Slide 2: Truth Tables – AND in ROM
Useful representations for logical relationships
Can be stored easily in ROM
  Memory as Data O.K., but Memory as Logic?
A | B | A AND B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Addr0 | Addr1 | Stored Bit
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Memorized, yes?
So, you stored a TT in your memory?

## Slide 3: Truth Tables – OR in ROM
Useful representations for logical relationships
Can be stored easily in a ROM
  Memory as Data O.K., but Memory as Logic?
A | B | A OR B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Addr0 | Addr1 | ROM Value
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Memorized, yes?
How much memory did it cost you?

## Slide 4: XOR Truth Tables & ROM
Useful representations for logical relationships
  Which one here?
Can be stored easily in ROM – can you build this TT & Circuit?
Did you know equality is XOR with negation?
  Q: But what else does XOR do for us, on its own?
A | B | A XOR B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Notes: A: addition. 0 + 1 is? 0 + 0 is? 1+1 is?

## Slide 5: TODO: Consider XOR
Combinational Circuits
Boolean Algebra
/* This is our first, non-atomic, combinational circuit */
Build the TT now for only two inputs {A,B} and one output X.
Then, the Function F(A,B) is just the OR of the rows with ones in the output column X.
Now, a circuit? Build this from either spec (1) or (2)
Circuit
Truth Table
Boolean Function
1
2
3

## Slide 6: Introduction to Boolean Algebra
This is binary algebra, or logical algebra
  We’re all good at math, right? How hard can two values be?
    We have a 50% chance of getting the “answer” right, yes?
      Algebra for dummies?
Rather than a spectrum of values [0, 32563] just 0 and 1
  Algebra for switches, transistors, machines!
    At one point, the algebra of the future.
    A Mathematical language for programming (ProLog, etc.)
      For us, it is the algebra of life presently in this class.
        Q: At another point, the algebra of the past?
Notes: A: Doubt it.

## Slide 7: Boolean Definitions (Cheat Sheet)
Circuit
Truth Table
Boolean Function
Concept Name | Definition
Boolean Operators (BO?) | AND, OR, and NOT (same as in CS1 or Phy101)
Boolean Expression (BE) | Combination of Boolean Variables and Operators, e.g. “A + B”
Truth Table (TT) | Tabular, exhaustive mapping of inputs and outputs to describe some simple operation (an operator, also any algorithm)
Combinational Circuit (CC) | Circuit schematic defining outputs in terms of inputs and some combination of atomic circuits elements (mirrors BOs)
Boolean Function (BF) | Outputs defined via inputs and either a {BE, TT, CC}
Boolean Laws or Identities | Govern the transformation and simplification of BE/BFs & CCs, whereas TTs are complete, possibly redundant, never simplified)
Precedence, Order of Ops | NEGATION, AND, OR
Boolean Function
Boolean Equation
(variables & operators)
Truth Tables
(Maps of all IO Combinations)
BO
{AND, OR, NOT}
Arbitrary Algorithm
Notes: Note that the circuits are stateless or memory-less here. Note the use of Stacks and Venn Diagrams – google anything you don’t know.

## Slide 8: Boolean Definitions Explained
A Boolean Expression: A combination of variables and operations over those variables {AND, OR, NOT}
  There exists a unique and standardized form for all equations
A Boolean Function: F(a,b,c) = output{x,y,z}
  An expression in terms of one or more inputs (a,b,c) that produces some output {x,y,z} based on the inputs
    The definition of a combinational circuit is just this
      Whereas a sequential circuit chooses an output based on its inputs and some sequence of (saved) states (ie, memory)
AND(A,B) = AB, or we could view this function/mapping as a Truth Table
  A Truth Table is just a brute force enumeration that exhaustively shows the relationship between the input value set and the output results for all possible input configurations
Circuit
Truth Table
Boolean Function
Notes: Note that the circuits are stateless or memory-less here.

## Slide 9: Expanding on Truth Tables: ROM or Gates?
Circuit
ROM
Truth Table
Q: What is the difference between a circuit and a truth table?
  Are they equivalent logically?
Q: What is the difference then, between a truth table stored in one format versus another?
  Circuits realize Boolean logic directly as hardware
  Circuits realize Memory (ROM)
  ROM can encode Boolean logic via one level of indirection (an address)
    The address to a rom could be the input values for two wires, A and B
      A = Addr0, B = Addr1
A | B | Stored ROM value
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0 //with carry
Notes: Different than Micro-OpCodes

## Slide 10: Big Idea: ROM (Acts) as Gates?
Concept: Memory can “remember” how a circuit behaves and act in it’s place (emulate)
  Just ask the memory rather than implement the hardware!
  Analogy: HAL versus HEL
  Analogy: Caching sine/cosine rather than calculating on the fly
    This uses the hardware once (expensive, long) and caches results in RAM (cheap, quick lookup)
Now before you think we’ve moved all gated hardware into some other format like “code”, I ask you…
  Q: What do you think memory is made of?
  Both circuits and memory are just gates; two sides of the same coin.
Notes: Different than Micro-OpCodes

## Slide 11: Positive Logic AND <-> Negative Logic OR
We can make an AND from an OR simply by reversing the logic scheme….wait a sec, like using a NOT?
  Also, now we see why NAND looks like AND in pos/neg logic
A | B | “A AND B”
0F | 0F | 0F
0F | 1T | 0F
1T | 0F | 0F
1T | 1T | 1T
A | B | “A OR B”
0T | 0T | 0T
0T | 1F | 0T
1F | 0T | 0T
1F | 1F | 1F
Positive Logic
Negative Logic
So if you’re on an island and all you have is AND and NOT, you have all you need to get to OR
“” because the 0,1 currents remain the same, the circuit stays the same but the meaning (interpretation) of the bits are flipped so AND behaves like OR when flipping from positive to negative logic
“Do you draw power from abilities, or voltage on a wire (electro v.s. learningGuy

## Slide 12: Summary of Boolean Laws
Law | AND * | OR +
Identity | 1 * A = A | 0 + A = A
Idempotent | A * A = A //grow or shrink | A + A = A
Inverse | A * ~A = 0 | A + ~A = 1
Domination | A * 0 = 0 //Null calls this “Null” | A + 1 = 1 //drives to 1 or 0
Commutative | A * B = B * A //move vars | A + B = B + A
Distributive | A * (B + C) = A * B + A * C | A + (B * C) = A + B * A + C
Associativity | A * (B * C) = (A * B) * C | A + (B + C) = (A + B) + C
DeMorgan’s | ~(A * B) = ~A + ~B //math girls | ~(A + B) = ~A * ~B
Compound Equalities | AND | OR
Combination of Laws #1 | A*B + ~A*B = (A+~A)B = B //must derive this first, then cite | A+B * ~A+B = (A*~A)+B = B //cannot cite without derivation
Combi Laws #2 | A*(~A+B) = A * B | A + ~AB = A + B //We’ll prove this
Combi Laws #3 | (A*B) + (~A * B) = B | (A + B) * (~A + B) = B //and this
Absorption | A*(A+B) = B //this proves OR too | A+(AB) = A
Notes: Have these laws memorized, please. I’ll prove some compound equalities now to show you some moves, and start you with some easier BEs to simplify.

## Slide 13: Laws of Complementation (Laws of Inverse or Negation)
Name | Example
1) Complement Definition (Not TRUE is FALSE) | If A = 1 then !A = 0 If A = 0 then !A = 1
2) A AND Complement of A (a & !a) | A * !A = 0 (related identity: A * 1 = A)
3) A OR Complement of A (a ¦ !a) | A + !A = 1 (related domination: A + 1 =1)
4) Double Negative (!(!a) | !(!A) = A
Examples
!!!!X == X
(Y * X* !Y) = (Y * !Y * X) = (0 * X ) == 0
(Q + R + !Q) == 1
Notes: Note that I’ve given the laws names rather than first law, second law, etc.

## Slide 14: Laws of Commutation (Laws of Commuting Variables with Like Signs)
Name | Example
Commuting with AND | A * B = B * A
Commuting with OR | A + B = B + A
Q1: Consider: A* B* C = A*C*B = C*B*A = …
Legal?
Q2: A*B+C = A*C+B = C*B+A = …
Legal?
(Summary: Watch your Signs)
Notes: A1: Yes
A2: No

## Slide 15: Laws of Associativity (Laws of Associating Parenthesis)
Name | Example
Associativity with AND | A * (B * C) = (A * B) * C
Associativity with OR | (A + B) + C = A + (B + C)
Q1: Consider: A * (B + C) = (A * B) + C
Legal?
  Try distributing on both sides
    We need a distributive law!
Notes: A1: No, since A * B + A * C != C+A * C+B

## Slide 16: Laws of Distribution (Laws of “Multiplying Out”)
Name | Example
Distribution with AND | A * (B + C) = (A * B) + (A * C)
Distribution with OR | A + (B * C) = (A + B) * (A + C)
Consider: (A * B) + C
What do you get if you distribute out?
  Can you move the first term (X = (A*B) )around?
    Try commuting the Boolean variables X and C
      Then distribute
Notes: C+A * C+B

## Slide 17: Laws of Tautology (Laws of Growing, Shrinking, & Obvious)
Name | Example
1) Anything AND itself is itself | A * A = A //grow or shrink
2) Anything OR itself is itself | A + A = A //either direction
3) A AND 1 is simply A | A * 1 = A
4) A AND 0 is simply 0 | A * 0 = 0
5) A OR 1 is simply 1 | A + 1 = 1
6) A OR 0 is simply A | A + 0 = A
More Examples
(A*A*A*A)+A = (A) + A == A
A * (1 + 0) = A
(A*!A) + A = A
A = A*1 = A*(B + !B) = AB + A!B //growing a term example
Notes: A’s overlap with the whole universe equals A
A’s overlap with null is void (*double points for author ref)

## Slide 18: Laws of Tautology (Laws of Obvious)
Name | Example
1) Anything AND itself is itself | A * A = A
2) Anything OR itself is itself | A + A = A
3) A AND 1 is simply A | A * 1 = A
4) A AND 0 is simply 0 | A * 0 = 0
5) A OR 1 is simply 1 | A + 1 = 1
6) A OR 0 is simply A | A + 0 = A
AND and OR act the same here
AND and OR act differently here
“AND and OR have a lovely, interrelated relationship.
AND can ground you to earth/0 while OR can lift you up to the universe” – Poetic Nash
“Given a set, what might you do with it? Determine if they’re all the same? Determine if just one is different? This is what AND-OR provides.” – Math Nash

## Slide 19: Laws of Absorption (Laws of “Least Obvious”)
Name | English Description | Example
Absorption with AND Distribution | Plug in 1 for A, notice the output is 1. Plug in 0 for A, notice the output is 0. The output is tied to the input A. | A * (A + B) = A //lets prove this and we’ll prove //below at the same time
Absorption with OR Distribution | Same description as above | A + (A * B) = A
Q1: Consider: A * ( A + B )
  What does this distribution give you?
Q2: Consider: C+A * C+B
  Reduce it? Sure: C + (A * B)
Notes: A*(A+B) -> (A*A)+A*B ->A+AB -> A(1+B) ->A(1) -> A
C+A * C+B -> C+(A*B)

## Slide 20: Laws of DeMorgan (De Morgan’s Theorems, or “Laws” of “Math” For Men and Women)
Name | Example
Compound Negation with AND | (A * B) = A + B
Compound Negation with OR | (A + B) = A * B
Examples
Consider: A * ( A + B )
  Simplify it and prove this is equal to A
    Show all work and cite all theorems using any name
Notes: NOT A OR NOT ( A + B )
NOT A OR (NOT A AND NOT B) //use which theorem here? X + (X * Y) == X

## Slide 21: “How To” Work With Binary Algebra
Have the laws by your side in a table (in these slides, text, etc.)
Practice applications of a law to a boolean expression
  If things don’t improve, try another law; in general, laws:
    Shrink a more complex expression into a simpler version
      Reduction trick: Consider more complex expressions as Boolean variables themselves!
        Example: XY + XY is just A + A which reduces to A which is XY
    Grow an expression to introduce variables in order to apply a different law and reduce further
      Expansion trick: Introduce new terms based on the inverse law
        Example: X == X * 1 == X * (A+ A) == XA +XA
ProTip: Look for Duplicates and Toggles
Notes: Expand to reduce: 3 steps forward and 2 steps back is still forward progress; sometimes you must get up to get down.
Knowing when to apply which law or trick is not so straightforward and requires experience & practice

## Slide 22: Grow? Make Things Bigger?
Yes, we grow locally (temporarily) to reduce globally (eventually).
  3 steps forward and 2 steps back is still forward progress
  Sometimes you must get up to get down.
Knowing when to apply which law or trick is not so straightforward and requires experience & practice
So lets practice our brains out!

## Slide 23: Boolean Exercise #1
F(X,Y) = XY + XY
  Show this is just XY by applying laws
    Show each step and cite the law you use
Can you prove this using a different set of steps?
  How many different ways?
Notes: Soln1A) Just use Identity
Soln1B) Use distribitutive then identity
Soln1C) Use DeMorgans, distributive, then DeMorgans

## Slide 24: #2: F(X,Y) = XY + !XY = ?
Law | AND * | OR +
Identity | 1 * A = A | 0 + A = A
More Identity | A * A = A | A + A = A
Inverse | A * ~A = 0 | A + ~A = 1
Domination | A * 0 = 0 | A + 1 = 1
Commutative | A * B = B * A | A + B = B + A
Distributive | A * (B + C) = A * B + A * C | A + (B * C) = A + B * A + C
Associativity | A * (B * C) = (A * B) * C | A + (B + C) = (A + B) + C
DeMorgan’s | ~(A * B) = ~A + ~B | ~(A + B) = ~A * ~B
Combinations | A*B + ~A*B = (A+~A)B = B | A+B * ~A+B = (A*~A)+B = B
:294
Y
Notes: Answer = Y

## Slide 25: Boolean Exercise #3
F(x,y,z) = xyz + xyz + xz
Law | AND * | OR +
Identity | 1 * A = A | 0 + A = A
More Identity | A * A = A | A + A = A
Inverse | A * ~A = 0 | A + ~A = 1
Domination | A * 0 = 0 | A + 1 = 1
Commutative | A * B = B * A | A + B = B + A
Distributive | A * (B + C) = A * B + A * C | A + (B * C) = A + B * A + C
Associativity | A * (B * C) = (A * B) * C | A + (B + C) = (A + B) + C
DeMorgan’s | ~(A * B) = ~A + ~B | ~(A + B) = ~A * ~B
Combinations | A*B + ~A*B = (A+~A)B = B | A+B * ~A+B = (A*~A)+B = B
Notes: Distributive
Inverse
Identity

## Slide 26: Answer for #3: F(x,y,z) = !xyz + !xy!z + xz
AND * | OR +
1 * A = A | 0 + A = A
A * A = A | A + A = A
A * ~A = 0 | A + ~A = 1 //shrinks terms
A * 0 = 0 | A + 1 = 1
A * B = B * A | A + B = B + A
A * (B + C) = A * B + A * C | A + (B * C) = A + B * A + C
A * (B * C) = (A * B) * C | A + (B + C) = (A + B) + C
~(A * B) = ~A + ~B | ~(A + B) = ~A * ~B
A*B + ~A*B = (A+~A)B = B | A+B * ~A+B = (A*~A)+B = B
!xy
True
!x(y (z +!z)) + xz
!xy + xz
False
x

## Slide 27: #4: F(x,y) = y + !x!y
y + !x
x
y
y + x
!y+ x
!y + !x
ProTip: Look for Duplicates and Toggles
Law | AND * | OR +
? | 1 * A = A | 0 + A = A
? | A * A = A | A + A = A //makes copies
? | A * ~A = 0 | A + ~A = 1 //makes toggles
? | A * 0 = 0 | A + 1 = 1
? | A * B = B * A | A + B = B + A
? | A * (B + C) = A * B + A * C | A + (B * C) = A + B * A + C
? | A * (B * C) = (A * B) * C | A + (B + C) = (A + B) + C
? | ~(A * B) = ~A + ~B | ~(A + B) = ~A * ~B
? | A*B + ~A*B = (A+~A)B = B | A+B * ~A+B = (A*~A)+B = B

## Slide 28: #5: F(x,y) = !x!y (!x + y) (!y + y)
z
1
!y!x
0
!x!y!x + !x*!y*y
!(x+y)
ProTip: L-to-R or R-to-L?
? | AND * | OR +
? | 1 * A = A | 0 + A = A
? | A * A = A | A + A = A
? | A * ~A = 0 | A + ~A = 1
? | A * 0 = 0 | A + 1 = 1
? | A * B = B * A | A + B = B + A
? | A * (B + C) = A * B + A * C | A + (B * C) = A + B * A + C
? | A * (B * C) = (A * B) * C | A + (B + C) = (A + B) + C
? | ~(A * B) = ~A + ~B | ~(A + B) = ~A * ~B
? | A*B + ~A*B = (A+~A)B = B | A+B * ~A+B = (A*~A)+B = B

## Slide 29: Boolean Exercise #6
Pen and paper first (exam practice), then on board together
F(x,y) = y + !(xy)
? | AND * | OR +
? | 1 * A = A | 0 + A = A
? | A * A = A | A + A = A
? | A * ~A = 0 | A + ~A = 1
? | A * 0 = 0 | A + 1 = 1
? | A * B = B * A | A + B = B + A
? | A * (B + C) = A * B + A * C | A + (B * C) = A + B * A + C
? | A * (B * C) = (A * B) * C | A + (B + C) = (A + B) + C
? | ~(A * B) = ~A + ~B | ~(A + B) = ~A * ~B
? | A*B + ~A*B = (A+~A)B = B | A+B * ~A+B = (A*~A)+B = B
ProTip: L-to-R or R-to-L?
Notes: True.

## Slide 30: Boolean Exercise #7 (3.7)
This next exercise can be reduced in more than one way!
  Complement first?
  Or Distribute?
  Or Witty Law?
  Infinite ways?
    Help! Tools!
F(x,y) = (x+y)(!x+y)
? | AND * | OR +
? | 1 * A = A | 0 + A = A
? | A * A = A | A + A = A
? | A * ~A = 0 | A + ~A = 1
? | A * 0 = 0 | A + 1 = 1
? | A * B = B * A | A + B = B + A
? | A * (B + C) = A * B + A * C | A + (B * C) = A + B * A + C
? | A * (B * C) = (A * B) * C | A + (B + C) = (A + B) + C
? | ~(A * B) = ~A + ~B | ~(A + B) = ~A * ~B
? | A*B + ~A*B = (A+~A)B = B | A+B * ~A+B = (A*~A)+B = B
Notes: =y

## Slide 31: Boolean Exercise #8
Pen and paper (D&D style), then on board.
F(x,y) = !x*(x+y) + (y+x)(x+!y)
? | AND * | OR +
? | 1 * A = A | 0 + A = A
? | A * A = A | A + A = A
? | A * ~A = 0 | A + ~A = 1
? | A * 0 = 0 | A + 1 = 1
? | A * B = B * A | A + B = B + A
? | A * (B + C) = A * B + A * C | A + (B * C) = A + B * A + C
? | A * (B * C) = (A * B) * C | A + (B + C) = (A + B) + C
? | ~(A * B) = ~A + ~B | ~(A + B) = ~A * ~B
? | A*B + ~A*B = (A+~A)B = B | A+B * ~A+B = (A*~A)+B = B
Q: Short Path or Long Path?
Short Path
Long Path
ProTip: L-to-R or R-to-L?
Notes: Short Path: Laws of least obvious
=x+!xy //use absorption here
=x + y

## Slide 32: More Practice - Go!
Use Exercises
Use End of Section questions
Use End of Chapter questions

## Slide 33: Aside: What’s in a name? XNOR?
And then Not == NAND
Or then Not == NOR
XOR then NOT == ? //why?
  So if you see any NXORs in my slides, a reaper
    If you see any nx starships, also a reaper
      I’m not a robot
        Click on all NX class starships

## Slide 34: Infinite Diversity In Infinite Combinations
A single circuit has infinite realizations that are logically correct.
  But just like fish in the sea…
We will build a logically equivalent XNOR in multiple ways
  Actually, there exists infinite ways, but most are redundant and wasteful
And, given code that is O(n) for c=10, k=1, we know c=11, k=1 as well
  There exists infinite witnesses, although not all are as “tightly bound” or succinct
F(X) = X == X * 1 == X * X * 1 == X * X * (Y + Y) == …
  But as you can see, not all solutions would be simple or cost effective w.r.t. gates, just like the above solutions aren’t all optimal
Notes: …some stink worse than others.

## Slide 35: Canonical Form
We would like a unique representation of any Boolean expression
  This will allow us to compare two expressions and see directly if they are logically equivalent
  Also provides a standardized form to routinely process these equations
    Q: Why might we want this?
      Same Q: What is a solver? A 3SAT?
        A: As complexity increases, we need tools to uniformly process our designs and remove redundancies (we’ll do K-Maps by hand)
Just as DBs like PKs
  MS likes GUIDS
    ISTs for Compilers want distinct parse trees
There are a number of ways to produce a standardized form, and designers use different notations (get used to this type of complexity)
  Sum-of-Products: A bunch of terms ORed together
    F(x,y,z) = z + x!y!z == !x!yz + !xyz + x!y!z + x!yz + xyz
  Product-of-Sums: A bunch of terms ANDed together
S.O.P.
Simplest form rarely implies standard form and vice versa
Q: When using SOP or POS, you must still eventually reduce – why?
Q: SOP and POS are amenable to NAND and NOR gates – which and why?
A: We introduced redundancy to build a unique key, but this is not the least number of gates!
A: SOP has many more ANDs than or operations, POS has many more ORs than ands.
Notes: A: We introduced redundancy to build a unique key, but this is certainly not the least number of gates!
A: SOP has many more ANDs than or operations, POS has many more OR than ands

## Slide 36: S.O.P Example: Majority Function
To generate a SOP expression, just OR together all of the rows of the TT where the output (“Xout”) is equal to 1
Xout(x,y,z) = ?
x | y | z | Xout
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Q: What is a Majority Function?
  A: One of the commonly built combinational circuits
Xout(x,y,z) = !xyz + x!yz + xy!z + xyz

## Slide 37: Aside: Hardware Makes the Hero Super
Star Lord
Batman
Iron Man
RoboCop
Mr. Gadget
Who else?
Some people are good programmers, yet others are super!
  I wonder what could make such a difference?
    10k hours? This could help.
      Q: Will 10k hours with C help you write more efficient code for a specific platform?
    Rupture-and-Repair? Helps you reframe failure into success.
    Repeated “failures” often lead to success, like breaking a rock

## Slide 38: Aside: Hardware Makes the Hero Super
Star Lord
Batman
Iron Man
RoboCop
Mr. Gadget
Who else?
Notes: Some people are good programmers, and some are super programmers -

## Slide 39: Aside: Hardware Optimality
See PrinceOfHardware.pptx

## Slide 40: Hardware Problem Solving “How To”
Read the problem and determine inputs, outputs
Build the corresponding Truth Table enumeration
Build a Boolean Equation from the truth table
Reduce the Boolean Equation using Laws or K-maps
Build the optimal Circuit in simulator and test
Send this specification off to be pressed

## Slide 41: Summary of Boolean Laws
Law | AND * | OR +
Identity | 1 * A = A | 0 + A = A
Idempotent | A * A = A //grow or shrink | A + A = A
Inverse | A * ~A = 0 | A + ~A = 1
Domination | A * 0 = 0 //Null calls this “Null” | A + 1 = 1 //drives to 1 or 0
Commutative | A * B = B * A //move vars | A + B = B + A
Distributive | A * (B + C) = A * B + A * C | A + (B * C) = A + B * A + C
Associativity | A * (B * C) = (A * B) * C | A + (B + C) = (A + B) + C
DeMorgan’s | ~(A * B) = ~A + ~B //math girls | ~(A + B) = ~A * ~B
Compound Equalities | AND | OR
Combination of Laws #1 | A*B + ~A*B = (A+~A)B = B //must derive this first, then cite | A+B * ~A+B = (A*~A)+B = B //cannot cite without derivation
Combi Laws #2 | A*(~A+B) = A * B | A + ~AB = A + B //We’ll prove this
Combi Laws #3 | (A*B) + (~A * B) = B | (A + B) * (~A + B) = B //and this
Absorption | A*(A+B) = B | A+(AB) = A
Notes: Have these laws memorized, please. I’ll prove some compound equalities now to show you some moves, and start you with some easier BEs to simplify.

## Slide 42: Looking Ahead: K-Maps to the Rescue
Ever get stumped during a proof?
  Don’t know whether to reduce or expand?
The iterative application of these laws is cumbersome and not intuitive
  K-maps can help provide a repeatable process to determine the most efficient circuit for 2,3,4 variables
    5 or more variables can still benefit from K-maps, but they’re rarely made by hand
      A tool to build K-maps, where a K-map is a tool to simplify BE.