## Slide 1: CSS 422 Hardware and Computer Organization
Sequential circuit
Ver. 1
Senior Lecturer: Rob Nash
The slides are re-produced by the courtesy of Dr. Arnie Berger and edited by Wooyoung Kim and Rob Nash

## Slide 2: Before we start
Turn off your phone or at least sound off
Do not open your laptop, or turn on your computer unless you are asked to do
  Computers for class notes ONLY. Otherwise, I will consider you are distracting the class, and ask you to leave
  I tend to ask the students with the laptop open, just to see if you are following my lecture
No talk with your friends unless I ask to discuss
If I think you are distracting this class, I will ask you to leave the class
Warning: You will see this slide in EVERY class, because you keep forgetting to do so

## Slide 3: Topic
Sequential Circuit
  Chapter 4, 5 by Berger
  Chapter 11 by Stallings
  Flip-Flop
  Excitation table and K-maps
  Design registers

## Slide 4: Ex) 2-binary counter
Want to design a 2-binary counter system with logic gates.
2-binary counter:
  Input: one control bit
  The 2 bits are stored in the system
  If input is 0 then the 2 bits are unchanged
  If input is 1 then the 2 bits are counted up and if it reaches the maximum, then it resets to 0
Can we make with combinational logic gates?
What is it that the combinational circuit does not have, to design this system?

## Slide 5: Combinational vs. Sequential circuit
Combinational circuit
  The current output state depends only on the input states. It does not provide memory or state information, except ROM
Sequential circuits
  The current output depends on the current input, and on the past history of inputs
  The most common type of sequential circuit is the synchronous type
  Non-clocked Latch: asynchronous sequential circuit
  Edge-triggered flip-flop : synchronous sequential or clocked sequential circuit
  Interconnection of flip-flops and gates
Notes: So far, we have seen combinational circuits

## Slide 6: Asynchronous vs. synchronous
Asynchronous logic
  So far, we have seen asynchronous logic circuits.
  The change in the state depends on the input variables.
Synchronous logic
  With millions of logic gates, we need to synchronize the change of logic state with some master signal (clock).
  Suppose we need to move a data from a memory to register to do arithmetic addition. How the computer will know the sequence of the work?
  We need a system that works according to the order of tasks as time goes synchronous sequential circuit design

## Slide 7: Clocks and time
The clock in a digital system is an electronic analog of the pendulum which synchronizes the circuits in a computer system
  The master control signal
  Changes occur on the rising or falling edges of a clock pulse
Frequencies are the inverse of time (speed)
  Hz = the number of cycles per second: how to compute the time per each cycle?
  1 kilohertz ( KHz ) = 103 Hz ( cycle per second )
  1 megahertz (MHz ) = 106 Hz
  1 gigahertz (GHz) = 109 Hz
  1 terahertz (THz ) = 1012 Hz
Today the maximum PC clock frequencies are around 3.7 GHz

## Slide 8: Clocks and pulses
Clocks are continuous streams of pulses
Duty cycle = tPH / (tPH + tPL) x 100%
  The clock signal shown above has a 50% duty cycle
  The clock signal shown below has a 25% duty cycle
  Period: The time to complete one clock cycle
    Period = tcycle
  Frequency: The inverse of the period, f = 1/period
tPH
tPL
tcycle

## Slide 9: A real clock
Logic 0
Logic 1
Not Defined
Note that signal fidelity is not an issue. As long as the logic 1 is greater than 2.5 volts and logic 0 is less than 1 volt, the pulse will be properly interpreted
1V

## Slide 10: Pulse rise time measurement

## Slide 11: Propagation delay
Why can’t we simply rev-up the clock on your PC to 2 GHz, or higher?
  Answer: Gates require a finite amount of time to switch state when their inputs change
Consider the inverter gate, below:
The propagation delay (time delay from input change to output change),
Δt = 12.60ns

## Slide 12: Basic units for sequential circuit
Like the logic gates are the building blocks of combinational circuit, flip-flops are the building blocks of sequential circuit.
Flip-flops are built with logical gates
Before we study flip-flops, let’s start with a latch
Latch: Use feedback functionality
  Feedback: Bringing the output back to an input
  Locks the gate pair into a new state
  Transition is triggered by the application of the input pulse

## Slide 13: Latches
Need a circuit that remembers previous input values (states)
S-R Latch : has two stable states. (set/reset)
Regardless of previous states,
  When S is 1, Q becomes 1.
  When R is 1, Q becomes 0
  What if R=S=1, simultaneously? (race condition)
Notes: Assume Q=0, ~Q=1
Change R to 1, NOR out to Q becomes 0
Change R and S to 1, NOR out to ~Q becomes 1 and NOR out to Q is also 1? Bad logic, both hi
Then when RS go low, whichever signal actually goes low last will set the final value in the gate (hi or low, which is bad)

## Slide 14: Class exercise
Can you make a state table with the circuit diagram?
What is the characteristic table?
State table: truth table containing inputs and current state
  “Outputs” are the next state
Characteristic (state) table: Given the input lines and current state, determine next state (ie, next state is “output”)
  Excitation table: Start and end states are fixed; determine the signals required for the control lines to facilitate that transition (i.e. output is R,S signals)

## Slide 15
SR Latch

## Slide 16: Clocked SR Latches
SR Latch is an asynchronous operation, yet
Preventing the latch from changing state except at certain specific time.
  Only when Clock is 1, the latch is sensitive to S or R.
  How to resolve the undefined race condition for S=R=1?

## Slide 17
Avoid the SR latch’s instability by preventing the inputs being 1 at the same time.
In this case all possible combinations of input values are valid
Clocked JK Latch
Notes: Another useful flip-flop is the J–K flip-flop. Like the S–R flip-flop, it has two inputs. However, in this case all possible combinations of input values are valid. Figure 11.26 shows a gate implementation of the J–K flip-flop.

## Slide 18: Clocked D Latches
Avoid the SR latch’s instability by giving R as the inverse of S.
Stored value is available at Q
To load the current value of D, just give a positive pulse on the clock line.
What if D changes while the clock stays in HIGH (active)?

## Slide 19: Flip-Flops
Sometimes FF and latches are used as same in many books.
Flip-Flop: State transition occurs when the clock transition from 0 to 1 or from 1 to 0
Called a Flip-flop because the output Q is flip back and forth
Latch lacks a mechanism to shift control to the clock edge. The states change when the clock is active: called level-triggered
Take the JK clocked latch as an example. If J=K=1, and the clock is enabled, then it will flip continuously, and it is not we can control easily.
So, make the states change at the moment that the clock changes: called edge-triggered

## Slide 20: Latches and flip-flops
Basic components for sequential circuit design
They are bi-stable devices. It is in one of two states.
Without inputs, they remain in that state.
They have two outputs which are always the complements of each other.
Latch is level triggered while FF is edge triggered.
How to design the functionality of edge-trigger?

## Slide 21: Flip-Flops – cont’d
Delay in the inverter makes the circuit work.

## Slide 22
Standard D flip-flop.
Flip-Flops – cont’d

## Slide 23: Sequential circuit design
A sequential circuit can be a combination of combinational circuit and flip-flops
Because the sequential circuit involves state transition, we have different types of tables for this circuit
State table: Based on the input and current state, give the next state information (like truth table)
Characterization table: Give the state transition information based on inputs
Excitation table: Inputs are current and next state, and outputs are signals (S, R, J, K) why do we need this table?
Block diagram of sequential circuit

## Slide 24: Characteristic table for FF
Basic Flip-Flops and the characteristic table
Characteristic Table

## Slide 25: Excitation table for FF

## Slide 26: Excitation table
Excitation table (inverted characteristic table)
  input : a current state and next state
  output : S R or J K or D
Why we need this table?
FF is a feedback system. The transition information goes back to the states for inputs (S,R, etc)
Block diagram of sequential circuit

## Slide 27: Example of sequential circuit
Notes: If x is low, we OR A and B and output this as y
If x is high, we OR A and B and store this in DF(A) and store ~A in DF(B)

## Slide 28: When x is Low What Happens?
We ADD A and B and output this to y
We OR A and B and store this in D-FF(A)
We OR A and B and output this to y
We OR A and B and store this in D-FF(B)

## Slide 29: When x is High What Happens?
We OR A and B and store this in D-FF(B) and store ~A in D-FF(A)
We OR A and B and output this to y
We ADD A and B and store this in D-FF(A)
We OR A and B and store this in D-FF(A) and store ~A in D-FF(B)

## Slide 30: State Table
From the sequential circuit, can we build a state table?
When you get output?
In present? or in the next state?
A(t) | B(t) | (input) X | (output) Y | A(t+1) | B(t+1)
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0

## Slide 31: State Machine/Diagram
From the state table, can we build a state machine?
  States will be AB pairs
  Edges will be transitions based on input and describe I/O pairs
A(t) | B(t) | (input) X | (output) Y | A(t+1) | B(t+1)
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0

## Slide 32: State Machine/Diagram
A(t) | B(t) | (input) X | (output) Y | A(t+1) | B(t+1)
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0
From the state table, can we build a state machine?
  States will be AB pairs
  Edges will be transitions based on input and describe I/O pairs

## Slide 33: Design a sequential circuit
Design a sequential circuit
Draw a state diagram (state machine)
Figure out the input and outputs
Build a state table and derive an excitation table
Boolean function equation using K-map
A sequential circuit
Let’s design a 2-bit binary counter.
A sequence of repeated binary states 00, 01, 10, 11 whenever the input is 1.

## Slide 34
Let’s design a 2-bit binary counter.
A sequence of repeated binary states 00, 01, 10, 11 whenever the input is 1.
Notice how the output is embedded in the current state
  A Moore Machine
We could encode output on edge transitions, too
  A Mealy Machine
00
11
01
10

## Slide 35: 2- bit binary counter - state diagram

## Slide 36: 2- bit binary counter – input/output
Input (control signal): x
# of FF: 2 (2 bits)
Suppose we are using JK FFs.
Then we need two J’s and two K’s
In the state machine, you can build a state table
The next states connected to JK’s
So, we need extended table excitation table
Present state (t) |  | Input | Next state (t+1) | 
A | B | x | A | B
0 | 0 | 0 | ? | ?
0 | 0 | 1 | ? | ?
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 37: 2- bit binary counter – input/output
Input (control signal): x
# of FF: 2 (2 bits)
Suppose we are using JK FFs.
Then we need two J’s and two K’s
In the state machine, you can build a state table
The next states connected to JK’s
So, we need extended table excitation table
Present state (t) |  | Input | Next state (t+1) | 
A | B | x | A | B
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0

## Slide 38: 2- bit binary counter – excitation table
Present state (t) |  | Input | Next state (t+1) |  | Flip-flop inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 | 0 | 0 |  |  |  | 
0 | 0 | 1 | 0 | 1 |  |  |  | 
0 | 1 | 0 | 0 | 1 |  |  |  | 
0 | 1 | 1 | 1 | 0 |  |  |  | 
1 | 0 | 0 | 1 | 0 |  |  |  | 
1 | 0 | 1 | 1 | 1 |  |  |  | 
1 | 1 | 0 | 1 | 1 |  |  |  | 
1 | 1 | 1 | 0 | 0 |  |  |  | 
Q(t) | Q(t+1) | J | K
0 | 0 | 0 | x
0 | 1 | 1 | x
1 | 0 | x | 1
1 | 1 | x | 0
Given our present state, input, and all possible next states, what wires do I need to assert to accomplish this?
  Note our FSM/ASM defines the set of next states for a given state

## Slide 39: 2- bit binary counter – excitation table
Present state (t) |  | Input | Next state (t+1) |  | Flip-flop inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 | 0 | 0 | 0 | x | 0 | x
0 | 0 | 1 | 0 | 1 | 0 | x | 1 | x
0 | 1 | 0 | 0 | 1 | 0 | x | x | 0
0 | 1 | 1 | 1 | 0 | 1 | x | x | 1
1 | 0 | 0 | 1 | 0 | x | 0 | 0 | x
1 | 0 | 1 | 1 | 1 | x | 0 | 1 | x
1 | 1 | 0 | 1 | 1 | x | 0 | x | 0
1 | 1 | 1 | 0 | 0 | x | 1 | x | 1
Q(t) | Q(t+1) | J | K
0 | 0 | 0 | x
0 | 1 | 1 | x
1 | 0 | x | 1
1 | 1 | x | 0
You cannot control the next state: So, not an input nor an output

## Slide 40
Ja | ~A~B | ~AB | AB | A~B
~x |  |  | x | x
x |  | 1 | x | x
Ka | ~A~B | ~AB | AB | A~B
~x | x | x |  | 
x | x | x | 1 | 
Jb | ~A~B | ~AB | AB | A~B
~x |  |  |  | 
x |  |  |  | 
Kb | ~A~B | ~AB | AB | A~B
~x |  |  |  | 
x |  |  |  | 
Present state (t) |  | Input | Next state (t+1) |  | Flip-flop inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 | 0 | 0 | 0 | x | 0 | x
0 | 0 | 1 | 0 | 1 | 0 | x | 1 | x
0 | 1 | 0 | 0 | 1 | 0 | x | x | 0
0 | 1 | 1 | 1 | 0 | 1 | x | x | 1
1 | 0 | 0 | 1 | 0 | x | 0 | 0 | x
1 | 0 | 1 | 1 | 1 | x | 0 | 1 | x
1 | 1 | 0 | 1 | 1 | x | 0 | x | 0
1 | 1 | 1 | 0 | 0 | x | 1 | x | 1
Ja=Bx
Ka=Bx

## Slide 41
Jb | ~A~B | ~AB | AB | A~B
~x |  | x | x | 
x | 1 | x | x | 1
Kb | ~A~B | ~AB | AB | A~B
~x | x |  |  | x
x | x | 1 | 1 | x
Present state (t) |  | Input | Next state (t+1) |  | Flip-flop inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 | 0 | 0 | 0 | x | 0 | x
0 | 0 | 1 | 0 | 1 | 0 | x | 1 | x
0 | 1 | 0 | 0 | 1 | 0 | x | x | 0
0 | 1 | 1 | 1 | 0 | 1 | x | x | 1
1 | 0 | 0 | 1 | 0 | x | 0 | 0 | x
1 | 0 | 1 | 1 | 1 | x | 0 | 1 | x
1 | 1 | 0 | 1 | 1 | x | 0 | x | 0
1 | 1 | 1 | 0 | 0 | x | 1 | x | 1
Ja=x
Ka=x

## Slide 42: 2- bit binary counter-sequential circuit

## Slide 43: Examples of sequential circuit

## Slide 44: The “D” FF as a counting element
A 16-bit binary ripple counter
  Given the name because the pulses “ripple” through the circuit
Clock in
S
R
D
CLK
Q
Q
S
R
D
CLK
Q
Q
S
R
D
CLK
Q
Q
Q1
Q2
Q3
1
RESET
S
R
D
CLK
Q
Q
Q0
Each “D” FF divides the incoming clock frequency by 2X
RESET sets all Q output to 0 without a clock signal (asynchronous)
Counts as fast as the first stage can toggle, but cannot be read until the count has rippled through to the last stage
Can build counter/dividers of any length, any binary divisor
  Clock frequency at output Q3 equals fClock in ÷ 16

## Slide 45: “D” FF as a shift register
S
R
D
CLK
Q
Q
Q0
S
R
D
CLK
Q
Q
Q1
S
R
D
CLK
Q
Q
Q2
S
R
D
CLK
Q
Q
Q3
Shift data in
1
Shift data out
Clock in
RESET
Shift register moves data through successive stages on each clock pulse
Used for serial data communications, multiplication ( why ?), image processing
Basis for UART ( Universal Asynchronous Receiver/Transmitter )
Data can be read in serially and then read out in parallel
Serial data communications limits the number of signal wires needed to transmit bytewide
data ( Example shown here is a nibble )

## Slide 46: “D” flip-flop as a storage register
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D0
D7
D1
D3
D2
D4
D5
D6
Q0
Q7
Q1
Q3
Q2
Q4
Q5
Q6
Clock in
D0 D1 D2 D3 D4 D5 D6 D7
INPUT DATA
OUTPUT DATA
D0 D1 D2 D3 D4 D5 D6 D7

## Slide 47: An 8-bit storage register
D0
D7
D1
D3
D2
D4
D5
D6
Q0
Q7
Q1
Q3
Q2
Q4
Q5
Q6
Clock in
D0 D1 D2 D3 D4 D5 D6 D7
INPUT DATA
OUTPUT DATA
D0 D1 D2 D3 D4 D5 D6 D7
8-bit
Storage
Register

## Slide 48: The storage register with busses
D0..D7
8
BUS: A grouping of “like” signals
Here we have Data In bus ( D0..D7)
and Data out bus ( Q0..Q7)
Busses are usually drawn with heavier
lines to differentiate them from
individual signal wires
8
Q0..Q7
D0
D1
D2
D3
D4
D5
D6
D7
Q0
Q1
Q2
Q3
Q4
Q5
Q6
Q7
Clock in
8-bit
storage
register

## Slide 49: More on storage registers
The storage register provides a stable location to store data moving along busses
  Data on busses are transitory
  Storage register width typically matches the width of the data path
    May be 4, 8, 16, 32, 64 or 128 bits wide
  Registers interface data between a computer and the outside world
  Registers are the key data holders in computers and microprocessors
    A computer’s architecture is often defined by organization of the storage registers
Two variety of storage registers: “D” type and Latch
  Latch is level sensitive, output follows input when control is 0, output is latched ( locked ) when control is 1 ( or vice versa )

## Slide 50: First in-first out ( FIFO ) data storage
D0
D15
16-bit
Latch
Stage
1
16-bit
Latch
Stage
2
16-bit
Latch
Stage
3
16-bit
Latch
Stage
N-1
16-bit
Latch
Stage
N
Control logic
Input bus
D0
D15
Output Bus
Clock in
Clock out
FIFO FULL
FIFO EMPTY
Latch controls
DATA FLOW

## Slide 51: Summary
Gate is a fundamental building block of all digital systems
Flip-flop is a basic unit for sequential circuit, which are built using gates and a clock
Design a sequential circuit system
  Draw a state diagram
  Draw a state table
  Build K-maps to derive Boolean equations
  Draw a circuit diagram based on the equations

## Slide 52: Next lecture
Bus organization and memory design
  Chapter 6 by Berger
  Chapter 3.4 by Stallings