## Slide 1: Building Memory
Instructor: Rob Nash
Readings: See schedule
“Quote”

## Slide 2
Image source: http://courses.cs.vt.edu/csonline/MachineArchitecture/Lessons/CPU/cpu_circuit.gif
Lets Focus on smaller RAMs and How to Scale RAM
A Simple RISC-Style Machine for Computation
A Smaller RAM Chip
(one package of 16 D-FFs)
A Larger RAM (Set of Chips)
(16 packages of the smaller RAM)

## Slide 3: From Smaller to Larger Chips
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
16-bit data bus, D0..D15
D0 D1 D2 D3 D4 D5 D6 D7 D8 D9 D10 D11 D12 D13 D14 D15
Q: How many bins (mappable locations) per chip? (word=16b)
Q: How many bytes total?
Expanding Memory Stride
Notes: A: 2^15
A: since both chips are in use to make a 16 bit bus, still 2^15

## Slide 4: Addressable Memory Defined
Address Space: the amount of externally accessible memory for a processor
If memory is just a matrix, the size of the address space is same as the number of rows in a matrix
  32K x 4 //32 x 210 rows where each row holds 4 bits
  The Address space describes the number of “bins”
    The number of slots, or number of things with mappable addresses
Total Memory Capacity is determined by the data width as well as the addressable memory space
  32K x 4 ==128K bits or 16KBytes in total
  16K x 8 == 8K x 16 == 4K x 32 == same Total Memory Capacity
Address bits are connected to decoder to turn on one of many things
  So k address bits can have 2k addressable bins

## Slide 5: Transistor Density Increase
Q: Can anyone guess the transistor count of the 68K?

## Slide 6
68,000
Notes: Source: Wikipedia

## Slide 7
RAM
(Volatile)
ROM
(Non-Volatile)
SRAM
(fast & large & expensive)
DRAM
(slow & small & cheap & refresh)
Memory
D
S

## Slide 8
RAM
(Volatile)
ROM
(Non-Volatile)
EDO
SRAM
(fast & large & expensive)
DRAM
(slow & small & cheap & refresh)
MDRAM
(multi-bank)
FPM
(Fast-Page Mode)
Synchronized
Memory
RDRAM
(rambus)
D
S
Notes: FPM is also just called Page Mode RAM, avoids an inefficiency in precharging a row with successive column accesses.
EDO is similar to FPM, but with an overlap (pipelining) in part of the accesses
MDRam is suitable for low end graphics cards, costs less than SRAM
RDRam lost to DDR in a standards war, even after Intel acquired Rambus (think: Beta vs VHS)

## Slide 9
RAM
(Volatile)
ROM
(Non-Volatile)
EDO
SRAM
(fast & large & expensive)
DRAM
(slow & small & cheap & refresh)
MDRAM
(multi-bank)
FPM
(Fast-Page Mode)
Burst EDO
SDRAM
(synchronous)
Synchronized
SL
(Synch-Link)
Memory
DR
(direct rambus)
RDRAM
(rambus)
D
S
DDR
(double data rate)

## Slide 10
RAM
(Volatile)
ROM
(Non-Volatile)
EDO
SRAM
(fast & large & expensive)
DRAM
(slow & small & cheap & refresh)
MDRAM
(multi-bank)
FPM
(Fast-Page Mode)
Burst EDO
SDRAM
(synchronous)
Synchronized
SL
(Synch Link)
Memory
RDRAM
(rambus)
SSRAM
(synch)
AS-SRAM
(asynch)
PB
(pipeline burst)
D
S
DDR
(double data rate)
DR
(direct rambus)
Notes: Hyphens.

## Slide 11
RAM
ROM
(Non-Volatile)
Memory
DRAM
SRAM
PROM
(programmable via blown fuses, one time)
EPROM
(Erasable Programmable, specialized tools, erase entire chip)
EEPROM
(Electrically Erasable Programmable, no specialized tools, erase 1b at a time)
Flash Memory
(Electrically Erasable Programmable, no specialized tools, block at a time, NAND and NOR)
Q: OK, Flash is a ROM?
A: ROM used to mean READ ONLY, but now means Non-Volatile
PROM Evolution over Time

## Slide 12
D0 D1 D2 D3 D4 D5 D6 D7
Data in/out (bidirectional) to Bus
A0 A1 A2 A3……….A15
Address Lines to Bus
Example: 512 Kbit Total Memory Capacity organized as 64K x 8
CS
OE
W
Memory Device Characteristics
0 == Writing to memory chip (storing)
A.k.a Inputting from the data bus
(Requires that the chip be on/selected)
(Requires data and address)
0 == Outputting our memory to the Data Bus
A.k.a Recalling the value from our memory
(Requires that the chip be on/selected)
0 == Turn chip on
A.k.a. Select this Chip
Prereq for any IO
!W, !CS, !OE live in the Control Bus

## Slide 13
Write Enable
Active low
Active on WRITES
D0 D1 D2 D3 D4 D5 D6 D7
Data in/out (bidirectional)
Typically 4, 8, 16, 32 bits wide
A0 A1 A2 A3……….A15
Address is unidirectional
Used for READS or for WRITES to memory
Q: Why 16 lines?
0000 0000 0000 0000
1111 1111 1111 1111
0000 0000 0000 0001
1111 1111 1111 1110
0000 0000 0000 0010
1111 1111 1111 1101
0000
0001
0002
(HEX)
FFFD
FFFE
FFFF
CS
Chip Select
Active low
Master switch for device
OE
Output Enable
Active low
Active on READS
W
Example: 512 Kbit device organized as 64K x 8
(Original Source: Arnie Berger)
Memory Device Characteristics (old)
…

## Slide 14: NEC SRAM
μPD444008
4Mb CMOS Static RAM
Exposed as 512Kx8
  Inside, a huge XY
Has a global !CS
Commercially available
  μPD444008-8
  μPD444008-10
  μPD444008-12
  Q: What are these?
All of this is invisible to programmers
A: Access times in nanoseconds
Notes: From characteristics to a real memory array
Guest chip! An Embedded SRAM

## Slide 15: From SRAM (Embedded) to Extendable DRAM (PC)
Architecture “hopping” here to showcase RAM similarities.
The total size above is 64MB (64M x 8b) for the master chip
Q: Notice anything below? Why the RAM “covers”?
A: heat sinks, and the master chip is composed of multiple subchips, and they may differ in stride and capacity!
A: 16 subchips that are each 1M x 32b (==24 * 220 * 22 Bytes)
Static over Dynamic

## Slide 16: Memory Extension (XY)
Now, suppose you want to build a memory with the capacity of 32 X 8 bits
But, you have a number of 16 X 4 (nibble) memory chips
How to arrange the small chips to have a 32 X 8 memory?
32 X 8
16 X 4

## Slide 17: Memory Extension (Y x X)
Y-Axis
X-Axis
Increase the Address Space vertically
Increase the Data Stride horizontally
32 X 8
16 X 4
16 X 4
16 X 4
16 X 4
Q: How can the two of the 4-bit RAMs connect to form 8 bits?
Alt-Q: How can two pairs of 4 address lines map to 5 address lines?
Page 0
Page 1
  A: Split the chips up into pages
  A: Use the first (or last) line to select the page
    (low versus high order interleaving in Null)
16 X 4
?

## Slide 18: Extending Memory Addresses
Large memories can be constructed by combining smaller memory chips
Suppose you want to have a memory with the capacity of 32 X 8
  But, you have a number of 16 X 8 memory chips
  How to arrange the small chips to have a 32 X 8 memory?
You extend your systems RAM by adding more DIMMs
Q: How might a DIMM extend itself? A: The same method.
Q1: How many pins (address lines) does the smaller chip have?
Q2: The larger?
32 X 8
16 X 8
A0
A4
D0
D7
A0
A3
D0
D7
8
8
8
8
A: Fit the smaller memory into the larger.
Q3: But how would you arrange this?
A1: 4 for 16 bins
A2: 5 for 32 bins.
Notes: Q: Or, how many address in lines does the smaller chips have?
Q: The larger chip?

## Slide 19: Paging Example
Page 0 (16x8)
Page 1 (16x8)
Q: How can we map the outer 5 address lines (A0-A4) to the two smaller chips?
A4
A3
A2
A1
A0
A3
A2
A1
A0
A3
A2
A1
A0
CE
CE
A4 is Page/Chip Select
?
What's inside this?
1x2
Decoder
Rule: if you can make it, you can black box it
Adding Pages of chips in the Y-Axis Increases…
the # of Mappable Locations, thus Total Memory Capacity
the number of address wires to pick a page
Address
Space

## Slide 20: Y by X Memory Dimensions
Y
Ax
i
s
-Addr Bus
X Axis Determines Data Stride or Word Length (Data Bus)
Determines the depth of the Address Space thus size of the Address Bus
16 X 4
16 X 4
16 X 4
16 X 4
Y locations & X bits per location
Q: What is the depth & width here?
Consider various Y x X configurations:
64M x 8 //64MB
4G x 32 //16GB as 4Gx4B
16M x 16 //32MB
128K x 128 //Vector proc, VMEM
Depth(Y) x Stride(X)

## Slide 21: Exercise #1
Each memory chip can be expressed with its capacity (addressable spaces x data bits) in bits
Y x X capacity indicates Y addressable spaces each with X data bits
Q: How many address lines and input-output data lines are needed for each of the followings capacity of memories?
64 addressable spaces at 32 bits wide (no byte-selection here)
  Q: How many address lines?
  Q: How many IO data path lines?
A 2K X 16b chip, without byte-selection
  Q: How many address lines?
  Q: How many IO data path lines?
  Q: What if we desired byte-selection? How would that affect our busses?
11A: 26 == 64, so 6 addr lines
12A: 32 bits == 32 data lines
21A: 210 * 21 == 11 addr lines
22A: 16 bits == 16 data lines
23A: 2 Bytes == +1 addr line

## Slide 22: Exercise #2 (is 2-Person)
Each memory chip can be expressed with its capacity (addressable spaces x data bits) in bits
Y x X capacity of memory indicates Y addressable spaces each holding X-bits of data
Q: How many data IO lines are needed for each chip below?
Q: How many address lines are needed for each chip below?
(Express answers in Y x X)
512K X 16 //no byte selection for any of these
16G X 8
32M X 32
128M X 64
A1: 219, so 19 addr x 16 data
A2: 234, so 34 addr x 8 data
A3: 225, so 25 addr x 32 data
A4: 227, so 27 addr x 64 data

## Slide 23: Null Interleaving Example
Assume a 128 x 32 bit memory (no Byte Select)
  Built using smaller N x 32 memory chips
    This is called “interleaving” memory chips in Null’s text
If we want an “8-way interleaved memory”
  Just a memory built with 8 pages in other terminologies
Assuming 8 smaller chips (one per page)…
Q1: What should their size N be to fill the larger memory?
Q2: How many address bits to you need to pick from N things?
Q3: How many page bits to pick from amongst 8 chips/pages?
Q4: What is the size of the total address space of the small chip?
Q5: What is the size of the total address space of the large chip?
Q6: How many address bits are needed for the large chip?
“Right into your memory banks”
128 x 32
Nx32
Nx32
Nx32
Nx32
Nx32
Nx32
Nx32
Nx32
A1: 128 slots/8 chips = 16 addressable slots per smaller chip
Outer Address (7)
(Low Order Interleaving)
Page(3)
Offset(4)
MSB
LSB
A2: Log216 = 4 address lines per smaller chip (a.k.a. offset bits)
A3: Log28 = 3 page bits to select one of 8 pages/chips (using a decoder)
A4: (smaller) 16 x 32b = 24 slots * 25 bits = 512 bits = (/8=64 Bytes)
A5i: (larger) 27 slots * 22 Bytes = 512 Bytes = 4Kbits
A5ii: (larger) 8 chips * 64 Bytes each = 512 Bytes
A6: Log2128 = 7 address lines (page(3) + offset(4))
A5: (larger) 128 x 32b = 27 slots * 25 bits = 4Kbits (/8=512Bytes)
16x32
16x32
16x32
16x32
16x32
16x32
16x32
16x32
64 Byte
512 Byte
Notes: No Byte Selection Here

## Slide 24: Low V.S. High Order Dictates Access Patterns
Low
Order
0,0,0,0
1,1,1,1
7,7,7,7
2,2,2,2
3,3,3,3
High
Order
0,1,2,3
4,5,6,7
4,5,6,7
4,4,4,4
5,5,5,5
6,7,7,7
There are performance considerations for both configurations
Consider multiple 8 element arrays (colored indices here)
Low-order interleaving
  Consecutive addresses in memory will be stored in different memory chips/banks/pages
    Perf: we can access neighboring elements in parallel (all 8 here)
High-order interleaving
  Consecutive addresses in memory will be stored consecutively in a chip (overflow goes to the next chip)
    Perf: caches can prefetch sequentially neighboring elements.
RAM Address using High-Order Interleaving
Byte Selector bits(1)
Page bits (5)
Offset bits(7)
RAM Address using Low-Order Interleaving
Byte Selector bits(1)
Page bits (5)
Offset bits(7)
0,1,2,3
0,1,2,3
4,5,6,7
0,1,2,3
4,5,6,7
BS?

## Slide 25: Byte Addressable V.S. Word Addressable
Address | Contents (0x)
0x0 | FA
0x1 | AA
0x2 | 10
0x3 | 1F
Byte-Addressable Memory (x1)
Addresses move in multiples of 1, with every byte being targetable
Fetching the contents at 0x2 delivers the byte holding value 0x10
Address | Contents (0x)
0x0 | FA
0x1 | AA
0x2 | 10
0x3 | 1F
Addresses are issued in multiples of 2, with each word being targetable (aligned access)
Fetching the contents at 0x2 delivers the word 0x101F
  Use masks/shifting to isolate bytes
Writing to address 0x2 writes to 0x3 as well!
Fetching address 0x1 or 0x3 is nonaligned
Bytes are the smallest addressable collection today
Words are the “default” size of your machine’s operations
  Composed one or more bytes (2 here), machine specific
Word-Addressable Memory (x2)
More than words

## Slide 26: Consider 3 Lines (Address or Byte Select)
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
No address lines here, all 3 lines select one byte from 8
A mix of address/page selection bits and byte selector bits (2,1)
All address bits are used to define the max number of mappable bins, where each bin holds one byte (3 addr bits, no BS bits)
3
1
0
3
2
0
Just 3 address lines means…
A limited amount of mappable memory
A limited number of ways to subdivide this memory & it’s control logic
32x8
32x8
32x8
32x8
32x8
32x8
32x8
32x8
One address/page selection bit and two byte selector bits (1,2)
2
1
Same Area == Same amount of RAM
Notes: Consider just one of the 32x8 Black boxes to dive into here

## Slide 27: Selecting Bytes
RAM
ROM
(Stride)
(Depth)
Example: Given a 128 x 4 bit chip….
  Q1: What’s the total storage capacity, in bits?
  Q2: What is k (# of addr lines) assuming we can nibble select?
Next, consider a chip that is 512 total bits divided into 8 data lines
  Q3: How many addressable slots for 512b total and byte-sized words?
  Q4: What is k, the number of addr lines?
Next, assume a 512K x 16b chip, and word-selection (not byte-selection).
  Q5: What's the size of the address bus? How many data bus?
  Q6: Now, same chip but with the ability to byte-select?
A1: 128 slots * 4 bits == 512b total
A2: 2^7 == 128, so 7 addr lines to pick
A3: 512/8 == 2^9/2^3 == 2^6 bins/slots
A4: 6 address lines to pick from 2^6
A5: 19 addr lines, 16 data lines
A6: 19 addr lines + 1 byte select line
Notes: \

## Slide 28: High & Low Order Example
Byte Select
Chip/Page Select
Assume a 4K x 16 word memory
Build a 32-way interleaved memory
  Just a memory built with 32 pages in other terminologies
Assume we have only N x 8 chips, where you can pick N
Q: What should N be to support 32 pages of chips?
Q2: How many bits needed to pick from amongst 32 pages?
Q3: How many bits do we need if we want byte addressing?
Q4: Show the address assuming high-order interleaving
  Q: Msbs do what?
  Q: Lsb does what?
Q5: Now show the address using low-order interleaving
    Locality: consider an array: if the low-order bits specify the page, then successive elements are stored across multiple memory banks and may be accessed in parallel.
Non-matching Data Strides
Byte Addressable
4Kx16
Nx8
Nx8
Nx8
Nx8
Nx8
Nx8
…
…
…
…
RAM Address using High-Order Interleaving
Byte selector bits(1)
Page bits (5)
Offset bits(7)
A1: N should be 4K/32 = 27 or 128 addressable locations per smaller chip
A2: for 32-way interleaved memory, we need 5 page bits to select from 32 pages
A3: Each location stores 2 Bytes, so we need 1 extra address wire to control BS
RAM Address using Low-Order Interleaving
Byte selector bits(1)
Page bits (5)
Offset bits(7)
128x8
128x8
128x8
128x8
128x8
128x8
128x8
128x8
Notes: N==128, since 32*128 == 4K
Page: 5, Offset:7 BS: 1

## Slide 29: Lower Order Exercise
Meta-Address Bits w Byte Selection
Meta-Address Bits (no BS)
Build a 2048 X 32 memory using 256 X 8 memory chips with and without byte-selection.
  Q1: How many address lines and data lines in the 256 X 8 chips?
  Q2: How many address lines and data lines in the 2048 X 32 memory?
  Q3: What n-way interleaving is this? (i.e. How many pages?)
  Q4: How many chips per page?
  Q5: How many 256 X 8 memory chips you should have total?
    Divide larger memory bits by smaller memory bits
  Q6: Draw the smaller chips in rows inside the larger chip; how many per “row” or page?
Smaller Addr Lines
Smaller Addr Lines
Page bits
BS
Page bits
A1: 256 = 28 so 8 address lines and 8 data lines
A2: 2048= 2K = 2*210=211 so 11 address lines and 32 data lines
…
A3: 2K/256 = 211 / 28 = 23 pages of chips, so 8 way interleaving
A4: Smaller data stride is x8 and the larger is x32, so 4 chips per page
A5: 8 pages of chips where 4 chips per page, so 32 chips total
Alt: 211*22 Bytes / 28*1Byte =213/28=25 = 32 chips
Page 0
256x8
256x8
256x8
256x8
Notes: 4 chips per page and 8 pages

## Slide 30: Guest Memory Chip Characteristics
(Add this later, redundant)
32K x 8
A0
A14
…
D7
D0
Address interface is 15 lines for 32K bins
(one-way Addr Bus)
Idea: Build a larger memory chip in terms of data stride. 8b->16b?
Idea: Build a larger memory with in terms of addressable bins? 32K-> 64K?
~CS
~OE
Smaller memory data interface is 8 lines
(attaches to the Bi-Directional Data Bus)
Control logic is 2 lines (Active low; Control Bus)
Interfacing Smaller Memory to Larger Chips Big Ideas
~W
Notes: A: CE( chip enable) OE (output enable, read vs write)
A: cut-and-paste

## Slide 31: Y & X Dimensions Scale Memory
Y
Ax
i
s
Add
r
X Axis Determines Data Stride or Word Length
Determines the depth of the Address Space
Consider various Y x X configurations:
64M x 8 //64MB
4G x 32 //16GB as 4Gx4B
16M x 16 //32MB
128K x 128 //Vector proc, VMEM
32K x 8
A0
A14
…
D7
D0
Depth(Y) x Stride(X)
Q1: What if we wanted our chip to have a larger data stride, such as the 16b word on the M68K (external bus)?
Q2: What if we wanted our chip to have more addressable bins, such as the 16M locations found on the 68K?

## Slide 32: Cut-and-Paste (in X) To Expand IO Width/Stride
32K x 8
A0
A14
…
D15
D8
32K x 8
A0
A14
D7
D0
Data IO upgraded to 16b
By adding more chips in the X dimension, we upgraded our word size to 16b
We want our chip to have more than one page, so that the total RAM is 64Kx16 Q: How do we add a page here?
A: you already cut and paste in the x dimension, now do so for the y
X Axis Determines Data Stride or Word Length
A Page
(a logical set
of chips that
increases
data stride)
Page Interface(15)
A0
A14
…
…

## Slide 33: Cut-and-Paste (in Y) To Expand Address Space
32K x 8
A0
A14
…
D15
D8
32K x 8
A0
A14
…
D7
D0
32K x 8
A0
A14
…
D15
D8
32K x 8
A0
A14
…
D7
D0
Page 1
Q: How do we control page selection (in the y) or byte selection (in the x)?
15+
Page 0
A0
A14
Q: How do we pick a page/row?
(hint: decoder)
A15
16+
?
A: Add a 1:2 decoder and wire to pick
~CS
~OE
~CS

## Slide 34: Outer Memory Interface: (Inner Memory Address Wires + Control Wires)
A15
Page 1
Page 0
32K x 8
A0
A14
…
D15
D8
32K x 8
A0
A14
…
D7
D0
32K x 8
A0
A14
…
D15
D8
32K x 8
A0
A14
…
D7
D0
Q: How do we control page selection (in the y) or byte selection (in the x)?
A0
A14
Q: Next, how do we pick or select a byte(column)? (hint: decoder)
16+
~CS
~OE
~CS
A16
17!
~OE
A: Add a 1:2 decoder and wire to pick
A: We control the larger chip via 17 “address” lines ( & control);
Address offset bits for the smaller memories (A0-A14)
a Page Selector (A15, turns on a whole row of chips)
a Byte Selector (A16 here, but typically lsb)

## Slide 35: Again: Decoding the Memory Space
Design the SRAM (64K x 16) memory system using 256K bit (32K x 8) SRAM chips
Data Bus: D0..D15
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
Address Bus: A0..A14
To uP
ADDRESS DECODE LOGIC
W
To uP
A15
?
OE
CE0
CE1
RD
WR
Map Wires for Address &
Control?
16
2
Different Interface

## Slide 36: Decoding the Memory Space
“on”, “read”, “write”
Design the SRAM (64K x 16) memory system using 256K bit (32K x 8) SRAM chips
Data Bus: D0..D15
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
Address Bus: A0..A14
To uP
ADDRESS DECODE LOGIC
W
To uP
A15
?
OE
CE0
CE1
RD
WR
?
32K X 8
32K X 8
32K X 8
32K X 8
Control Line Decoder
~OE?
~CS?
~CS
~OE
~CS
~OE
~CS
~OE
~CS
~OE
Map A0-A14 to smaller memory (offset bits)
Map A15 to page selection (Q: ~OE or ~CS or ~W?)
Map RD/WR to storing or retrieving (Q: ~OE or ~CS or ~W?)
Start with Black Boxes and drill down
Notice These Control Wires?
~CS
~CS
~CS
~CS
~CS
~OE
~W
Added ~W

## Slide 37: Decoding Memory
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
To uP
ADDRESS DECODE LOGIC
W
To uP
OE
CE0
CE1
RD
WR
Address Bus: A0..A14
A15
?
Data Bus: D0..D15
What do these do?
Q:What feeds these?
Design the SRAM (64K x 16) memory system using 256K bit ( 32K x 8 ) SRAM chips
Unbox Smaller Memory & drill down
Notice OE, CE, & W control lines here
\
“on”, “read”, “write”
~CS
~OE
~W

## Slide 38: Decoding Memory
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
A0
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
D0
D1
D2
D3
D4
D5
D6
D7
OE
CE
W
To uP
ADDRESS DECODE LOGIC
W
To uP
OE
CE0
CE1
RD
WR
Q: Can we access bytes in this system? If so, how?
Address Bus: A0..A14
A15
Page selection
Data Bus: D0..D15
What do these do?
What feeds these?
Page 0
Page 1
Notice how this example flips page axes?
Notice how we synthesize two redundant lines from one? (CE0|1)
Notice how W and OE are controlled by RD/WR?
What about this?
These control Data Bus IO
A: This memory system cannot address individual bytes – only words!
\
“on”, “read”, “write”
~CS
~OE
~W
Notes: If we looked inside the address decode logic, we would see A15 controls CE0, CE1 and RD,WR controls W,OE
BUT!

## Slide 39: Processor-to-Memory & Addresses
Suppose a µP has a 17-bit address bus and 16-bit wide data bus, and it has byte-addressable addressing. And this µP is connected to a memory system M which is built with 32K x 8 devices and uses high-order interleaving.
µP
External View
of an
Address Ignores
Control Wire V.S.
Address Wire
Distinction
Divide the Outer, Local
Memory Interface Into
Three Groups
{Page, Offset, BS}
17
15
1
1
Byte selection (LSb)
Page selection (MSb)
1 | 15 | 1
Page | Offset | byte
lsb
msb

## Slide 40: Introduction to Assembly on the 68K
Lets become coding masters!
  Full speed ahead!

## Slide 41: 404 Not Found
ERROR

## Slide 42: Processor-to-Memory Interface (Disassembler Trial Groups?)
Consider a group that may end up as your Disassembler team,
  Work together, but everyone will have their own clicker answer
After 5-8 minutes, vote on each answer
If you finish early, see exercise 5 & 6 & 7
# of addressable bins (larger)
--------------------------------------- = # of pages
# of addressable bins (smaller)
# of Bytes or bits (larger)
--------------------------------------- = # of chips
# of Bytes or bits (smaller)
# of chips
----------------------------- = chips per page
# of pages
If byte-selectable on an N x 8 system: addressable bins == addressable bytes == 2N
If byte-selectable on N x M where M >8 , this means:
more than one byte per page (could still be one chip per page)
# of mappable bins is less than 2N as lines must now be dedicated to Byte Selection
  In this example, 2 bits for BS, so 2(n-2) == 28 mappable bins, each holding 4B
Meta-Address Bits w Byte Selection
Meta-Address Bits (no BS)
Smaller Addr Lines
Smaller Addr Lines
Page bits
BS
Page bits
Page bits are on the low end?
Low-order interleaving.

## Slide 43: Address Space Partitioning (Group Question #1)
Build a 1GB memory (1G X 8 memory organization)
Use 4 MB memory chips.
  Q1: How many address lines (offset bits) for the smaller memory?
  Q2: How many address lines for the larger memory?
  Q3: How many 4 MB memory chips are used?
  Q4: How many chips per page?
  Q5: How many pages do you have?
  Q6: How many page selection bits?
# of addressable bins (larger)
--------------------------------------- = # of pages
# of addressable bins (smaller)
# of Bytes or bits (larger)
--------------------------------------- = # of chips
# of Bytes or bits (smaller)
# of chips
----------------------------- = chips per page
# of pages
Meta-Address Bits w Byte Selection
Meta-Address Bits (no BS)
Smaller Addr Lines
Smaller Addr Lines
Page bits
BS
Page bits
A1: 4Mx8 == 222, so 22 addr/offset lines
A2: 1Gx8 == 230, so 30 addr lines
A3: 1G/4M == 230/222 = 28 chips = 256
A4: One chip per page
A5: Same as the number of chips
A6: 2x == Y number of pages, or log2Y=x

## Slide 44: Group Exercise #2
Build a 1MB memory (1M X 8 memory organization)
Use 64KB memory chips.
  Q1: How many address lines for the larger memory?
  Q2: How many address lines for the smaller memory?
  Q3: How many 64 KB memory chips are used?
  Q4: How many pages you will have?
  Q5: How many chips per page?
  Q6: How many page selection bits you need?
  Q7: Draw the address using low-order interleaving.
Meta-Address Bits w Byte Selection
Meta-Address Bits (no BS)
Smaller Addr Lines
Smaller Addr Lines
Page bits
BS
Page bits
A1: 1Megax8 == 220 so 20 addr lines
A2: 64Kx8 == 216, so 16 addr lines
A3: 220/216==24, so 16 chips
A4: 16 pages
A5: 1 chip per page, since both are x8
A6: 4 page bits for 16 pages

## Slide 45: Processor and Memory #3
Suppose a µP has a 17-bit address bus and 16-bit wide data bus, and has no byte-addressable addressing. And this µP is connected to a memory system M which is built with 32K x 8 devices.
  Q1: How many address lines and data lines at µP?
  Q2: What is the total capacity of the µP? (the total number of bytes to fill the address space)
  Q3: How many address lines and data lines in the smaller memory? (How many address lines and data lines per 32K x 8 chip?)
  Q4: How many page selection bits in the memory system M?
  Q5: How many byte selection bits in the memory system M?
  Q6: How many of the smaller memory chips are in the µP?
  Q7: Draw the larger memory as pages of smaller memories.
# of addressable bins (larger)
--------------------------------------- = # of pages
# of addressable bins (smaller)
# of Bytes or bits (larger)
--------------------------------------- = # of chips
# of Bytes or bits (smaller)
# of chips
---------------- = chips per page
# of pages
If byte-selectable on an N x 8 system: addressable bins == addressable bytes == 2N
If byte-selectable on N x M where M >8 , this means:
more than one byte per page (could still be one chip per page)
# of mappable bins is less than 2N as lines must now be dedicated to Byte Selection
  In this example, 2 bits for BS, so 2(n-2) == 28 mappable bins, each holding 4B
A1: 17-bit address bus, so 17x16
A2: 217 bins, each holding 2 Bytes == 256KB
A3: 32K == 215, so 15 address lines
A4: 17-15 == 2 page bits. Or 128K/32K == 4 pages
A5: None, by definition
A5: 2 chip per page to match the x16 data stride
A6: 4 pages with 2 chips per page == 8

## Slide 46: Color Blind Example #4
A µP has 10-bit address bus and 32-bit wide data bus. Assume that you are accessing a memory system that has been built using 128 x 8 memory chips. The µP is byte-addressable.
  How many bits do you need for byte selection?
  How many offset bits do you need?
  How many pages do you have?
  Divide the 10-bit address lines into page number bits, offset bits and byte address bits.
  How many 128 x 8 memory chips do you need to completely fill the memory space of this processor?
  How much memory total does the processor have, in Bytes?
  Draw the configuration.
# of addressable bins (larger)
--------------------------------------- = # of pages
# of addressable bins (smaller)
# of Bytes or bits (larger)
--------------------------------------- = # of chips
# of Bytes or bits (smaller)
# of chips
----------------------------- = chips per page
# of pages
If byte-selectable on an N x 8 system: addressable bins == addressable bytes == 2N
If byte-selectable on N x M where M > 8, this means:
more than one byte per page (could still be one chip per page)
# of mappable bins is less than 2N as lines must now be dedicated to Byte Selection
  In this example, 2 bits for BS, so 2(n-2) == 28 mappable bins, each holding 4B
A1: 4 Bytes, so 2 BS bits
A2: log2128 = 7 offset bits
A3: 10-2-7 = 1 page bit for 2 pages or 210/27 =23 chips and if 4 chips/page, 2 pages
A4: (1)(7)(2)
A5: 4 per page & 2 pages = 8 chips
A6: 4 chips per row/page and 2 rows
page(1) | offset(7) | byte(2)
Page 0
128x8
128x8
128x8
128x8

## Slide 47: Page : Offset
What else?

## Slide 48: Paging
Processors with smaller address spaces can still manipulate larger memory arrays with techniques such as Paging
  Special memory or I/O location used to swap in and out memory pages
Hardware paging should not be confused with virtual addresses & VPaging
In the figure below, writing a data value to the page select register will cause a page swap to occur
Page Select
Register

## Slide 49: Paging
Hardware Addressing subdivides bits
Page 1
Page 0
Suppose a larger memory chip has 32 X 8 capacity.
An inner memory chip has 16 addressable spaces
You need 2 smaller pages to build the larger chip
How could we address data at 14 and 30?
  Method 1: Read an absolute address
  Address 14 = 01110
  Address 30 = 11110
  Method 2: Read with page number and offset, (assuming that 0 to 15 at the 0th page, 16-31 on the next page.)
    Address 14 = 0 1110 (page 0 : offset 1110)
    Address 30 = 1 1110 (page 1 : offset 1110)
Address Data
0
1
2
3
4
5
6
7
8
9 10 11 12 13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
0
1
2
3
4
5
6
7
8
9 10 11 12 13
14
15
0
1
2
3
4
5
6
7
8
9 10 11 12 13
14
15
Page #
Offset
Programmer View,
Absolute Address

## Slide 50: Address Space Partitioning Exercise
Using 1 KB master memory module built with a 128 x 8 chips
? bits for page selection.
? bits for offset (each page)
Page Selector (?-bits. Binary) | Offset Address (? bits. Binary) | Comments | Absolute Address (Dec)
 |  | First address: Page 0 | 
 |  | Last address: Page 0 | 
 |  | First address: Page 1 | 
 |  | Last address: Page 1 | 
 |  | First address: Page 2 | 
 |  | Last address: Page 2 | 
 |  | First address: Page 3 | 
 |  | Last address: Page 3 | 
… | … | … | …
Page 0
Page 1
Page 2
Page 3

## Slide 51: Partitioning Exercise
Page Selector (3-bits. Binary) | Offset Address (7 bits. Binary) | Comments | Absolute Address (Dec)
000 | 0000000 | First address: Page 0 | 0
? | ? | Last address: Page 0 | ?
? | ? | First address: Page 1 | ?
? | ? | Last address: Page 1 | ?
 |  | First address: Page 2 | 
 |  | Last address: Page 2 | 
 |  | First address: Page 3 | 
 |  | Last address: Page 3 | 
… | … | … | …
Page 0
Page 1
Page 2
Page 3
Using 1 KB master memory module built with a 128 x 8 chips
3 bits for page selection.
7 bits for offset (each page)
Complete Address

## Slide 52: Partitioning Exercise
Using 1 KB master memory module built with a 128 x 8 chips
3 bits for page selection. 7 bits for offset (each page)
Page Selector (3 bits. Binary) | Offset Address (7 bits. Binary) | Comments | Absolute Address (Dec) | Binary to Hex (R-to-L)
000 | 000 0000 | First address: Page 0 | 0 | 0x000
000 | 111 1111 | Last address: Page 0 | 127 | 0x07F
? | ? | First address: Page 1 | 128 | 0x080
? | ? | Last address: Page 1 | ? | 
 |  | First address: Page 2 |  | 
 |  | Last address: Page 2 |  | 
 |  | First address: Page 3 |  | 
 |  | Last address: Page 3 |  | 
… | … | … | … | 
Page 0
Page 1
Page 2
Page 3
000 0000
111 1111
000 0000
111 1111
000 0000
111 1111
001
001
010
010
011
011
255
256
383
384
511
?
?
?
+7F
+7F
+7F
+1
+1

## Slide 53: More Partitioning Exercises
Using 1 GB memories (30 bits) with a 4 MB chips (22 bits)
Page selector: (? bits)
Offset (the # address lines for each chip/page): ? bits
Page Selector (?-bits. Binary) | Offset Address (?-bits. Binary) | Comments | Absolute Address (Hex)
? | 00 0000 0000 0000 0000 0000 | First address: Page 0 | 00000000
? | 11 1111 1111 1111 1111 1111 | Last address: Page 0 | ?
? | 00 0000 0000 0000 0000 0000 | First address: Page 1 | 
? | 11 1111 1111 1111 1111 1111 | Last address: Page 1 | 
? | 00 0000 0000 0000 0000 0000 | First address: Page 2 | 
? | 11 1111 1111 1111 1111 1111 | Last address: Page 2 | 
. . | . . | . . | 
 | 00 0000 0000 0000 0000 0000 | First address: Page FF | 
 | 11 1111 1111 1111 1111 1111 | Last address: Page FF | 
Page 0
Page 1
Page 2
Page 255

## Slide 54: Address Space Partitioning
Using 1 GB memories (30 bits) with a 4 MB chips (22 bits)
Page selector: (8 bits)
Offset (the # address lines for each chip/page): 22 bits
Page Selector (8-bits. Binary) | Offset Address (22-bits. Binary) | Comments | Absolute Address (Hex)
00 0000 00 | 00 0000 0000 0000 0000 0000 | First address: Page 0 | 00000000
00 0000 00 | 11 1111 1111 1111 1111 1111 | Last address: Page 0 | ?
? | 00 0000 0000 0000 0000 0000 | First address: Page 1 | 
? | 11 1111 1111 1111 1111 1111 | Last address: Page 1 | 
? | 00 0000 0000 0000 0000 0000 | First address: Page 2 | 
? | 11 1111 1111 1111 1111 1111 | Last address: Page 2 | 
. . | . . | . . | 
 | 00 0000 0000 0000 0000 0000 | First address: Page FF | 
 | 11 1111 1111 1111 1111 1111 | Last address: Page FF | 
Page 0
Page 1
Page 2
Page 255

## Slide 55
Page Selector (8-bits. Binary) | Offset Address (22-bits. Binary) | Comments | Absolute Address (Hex)
00 0000 00 | 00 0000 0000 0000 0000 0000 | First address: Page 0 | 00000000
00 0000 00 | 11 1111 1111 1111 1111 1111 | Last address: Page 0 | 003FFFFF
00 0000 01 | 00 0000 0000 0000 0000 0000 | First address: Page 1 | ?
00 0000 01 | 11 1111 1111 1111 1111 1111 | Last address: Page 1 | ?
? | 00 0000 0000 0000 0000 0000 | First address: Page 2 | 
? | 11 1111 1111 1111 1111 1111 | Last address: Page 2 | 
. . | . . | . . | 
 | 00 0000 0000 0000 0000 0000 | First address: Page FF | 
 | 11 1111 1111 1111 1111 1111 | Last address: Page FF | 
Page 0
Page 1
Page 2
Page 255
Address Space Partitioning
Using 1 GB memories (30 bits) with a 4 MB chips (22 bits)
Page selector: 8 bits
Offset (the # address lines for each chip/page): 22 bits

## Slide 56: Address Space Partitioning
Page Selector (8-bits. Binary) | Offset Address (22-bits. Binary) | Comments | Absolute Address (Hex)
00 0000 00 | 00 0000 0000 0000 0000 0000 | First address: Page 0 | 00000000
00 0000 00 | 11 1111 1111 1111 1111 1111 | Last address: Page 0 | 003FFFFF
00 0000 01 | 00 0000 0000 0000 0000 0000 | First address: Page 1 | 00400000
00 0000 01 | 11 1111 1111 1111 1111 1111 | Last address: Page 1 | 007FFFFF
00 0000 10 | 00 0000 0000 0000 0000 0000 | First address: Page 2 | 00800000
00 0000 10 | 11 1111 1111 1111 1111 1111 | Last address: Page 2 | ?
. . | . . | . . | . .
? | 00 0000 0000 0000 0000 0000 | First address: Page FF | ?
? | 11 1111 1111 1111 1111 1111 | Last address: Page FF | ?
Page 0
Page 1
Page 2
Page 255
Using 1 GB memories (30 bits) with a 4 MB chips (22 bits)
Page selector: 8 bits
Offset (the # address lines for each chip/page): 22 bits

## Slide 57: Address Partitioning Done
Page Selector (8-bits. Binary) | Offset Address (22-bits. Binary) | Comments | Absolute Address (Hex)
00 0000 00 | 00 0000 0000 0000 0000 0000 | First address: Page 0 | 00000000
00 0000 00 | 11 1111 1111 1111 1111 1111 | Last address: Page 0 | 003FFFFF
00 0000 01 | 00 0000 0000 0000 0000 0000 | First address: Page 1 | 00400000
00 0000 01 | 11 1111 1111 1111 1111 1111 | Last address: Page 1 | 007FFFFF
00 0000 10 | 00 0000 0000 0000 0000 0000 | First address: Page 2 | 00800000
00 0000 10 | 11 1111 1111 1111 1111 1111 | Last address: Page 2 | 00BFFFFF
. . | . . | . . | . .
11 1111 11 | 00 0000 0000 0000 0000 0000 | First address: Page FF | 3FC00000
11 1111 11 | 11 1111 1111 1111 1111 1111 | Last address: Page FF | 3FFFFFFF
Page 0
Page 1
Page 2
Page 255
Using 1 GB memories (30 bits) with a 4 MB chips (22 bits)
Page selector: 8 bits
Offset (the # address lines for each chip/page): 22 bits

## Slide 58: Aside: Hard-Boiled Eggs
Image Source: http://lehacker.com/big-endian-little-endian-formats/

## Slide 59: Byte Addressing – Big Endian
This is a big-endian processor. Regardless, Word addresses will always be an even number:
8 data bits
8 data bits
8 data bits
8 data bits
16 data bits – 8 data bits/use
Page (A16) | Word Address (A16..A0) | D15…D8 | D7..D0
0 | 0x00000 | 0x00000 | 0x00001
 | 0x00002 | 0x00002 | 0x00003
 | 0x00004 | 0x00004 | 0x00005
 | .. | … | …
 | 0x0FFFE | 0x0FFFE | 0x0FFFF
1 | 0x10000 | 0x10000 | 0x10001
 | 0x10002 | 0x10002 | 0x10003
 | 0x10004 | 0x10004 | 0x10005
 | … | … | …
 | 0x1FFFE | 0x1FFFE | 0x1FFFF
1 | 15 | 1
Page | Offset | byte
Q: Where do we start reading for a given row? (For BS == 0)
A: From the “MSB” //consider an array of ascending values

## Slide 60: Byte Addressing – Little Endian
Q: Where do we start reading for a given row? (For BS == 0)
A: From the “LSB” //consider an array of ascending values
1 | 15 | 1
Page | Offset | byte
Page (A16) | Word Address (A16..A0) | D15…D8 | D7..D0
0 | 0x00000 | 0x00001 | 0x00000
 | 0x00002 | 0x00003 | 0x00002
 | 0x00004 | 0x00005 | 0x00004
 | .. | … | …
 | 0x0FFFE | 0x0FFFF | 0x0FFFE
1 | 0x10000 | 0x10001 | 0x10000
 | 0x10002 | 0x10003 | 0x10002
 | 0x10004 | 0x10005 | 0x10004
 | … | … | …
 | 0x1FFFE | 0x1FFFF | 0x1FFFE
8 data bits
8 data bits
8 data bits
8 data bits
16 data bits – 8 data bits/use
This is a little-endian processor. Regardless, Word addresses will always be an even number:

## Slide 61: Byte Packing – Big Endian
Byte 1 – Address 000001
Byte 0 – Address 000000
Byte 3 – Address 000003
Byte 2 – Address 000002
000000
Byte 1 – Address 000005
Byte 0 – Address 000004
Byte 3 – Address 000007
Byte 2 – Address 000006
000004
Byte 1 – Address 000009
Byte 0 – Address 000008
Byte 3 – Address 00000B
Byte 2 – Address 00000A
000008
Byte 1 – Address 00000D
Byte 0 – Address 00000C
Byte 3 – Address 00000F
Byte 2 – Address 00000E
00000C
Byte 1 – Address 000011
Byte 0 – Address 000010
Byte 3 – Address 000013
Byte 2 – Address 000012
000010
Byte 1 – Address FFFFF1
Byte 0 – Address FFFFF0
Byte 3 – Address FFFFF3
Byte 2 – Address FFFFF2
FFFFF0
Byte 1 – Address FFFFF5
Byte 0 – Address FFFFF4
Byte 3 – Address FFFFF7
Byte 2 – Address FFFFF6
FFFFF4
Byte 1 – Address FFFFF9
Byte 0 – Address FFFFF8
Byte 3 – Address FFFFFB
Byte 2 – Address FFFFFA
FFFFF8
Byte 1 – Address FFFFFD
Byte 0 – Address FFFFFC
Byte 3 – Address FFFFFF
Byte 2 – Address FFFFFE
FFFFFC
Byte Packing Definition: When the size of the data element (byte) is smaller than the width of the available memory (2B+), we use byte packing to save space
Read from Left to Right, or from the “Big End” of the Egg first
Longword
Address
D0
D7
D23
D31
“Read from the BIG side (MSB)”

## Slide 62: Byte Packing – Little Endian
Longword
Address
Byte 2 – Address 000002
Byte 3 – Address 000003
Byte 0 – Address 000000
Byte 1 – Address 000001
000000
Byte 2 – Address 000006
Byte 3 – Address 000007
Byte 0 – Address 000004
Byte 1 – Address 000005
000004
Byte 2 – Address 00000A
Byte 3 – Address 00000B
Byte 0 – Address 000008
Byte 1 – Address 000009
000008
Byte 2 – Address 00000E
Byte 3 – Address 00000F
Byte 0 – Address 00000C
Byte1– Address 00000D
00000C
Byte 2 – Address 000012
Byte 3 – Address 000013
Byte 0 – Address 000010
Byte 1 – Address 000011
000010
Byte 2 – Address FFFFF2
Byte 3 – Address FFFFF3
Byte 3 – Address FFFFF0
Byte 1 – Address FFFFF1
FFFFF0
Byte 2 – Address FFFFF6
Byte 3 – Address FFFFF7
Byte 3 – Address FFFFF4
Byte 1 – Address FFFFF5
FFFFF4
Byte 2 – Address FFFFFA
Byte 3 – Address FFFFFB
Byte 3 – Address FFFFF8
Byte 1 – Address FFFFF9
FFFFF8
Byte 2 – Address FFFFFE
Byte 3 – Address FFFFFF
Byte 3 – Address FFFFFC
Byte 1 – Address FFFFFD
FFFFFC
Byte-Packing Definition: When the size of the data element (byte) is smaller than the width of the available memory, we use this to optimize on space
D0
D7
Read from Right to Left, or from the “Little End” of the Egg first.
D23
D31
“Read from the LITTLE side (LSB)”

## Slide 63: Memory Organization & “Endian-ness”
Memory organization depends upon the width of the processor data bus
  The 68000 is a 32-bits for data internally
    But a 16-bit external data bus: can read 16-bits at a time
  All addresses are 32-bits internally, with 24-bits external (16M)
Bit
7
0
0x0000
0xFFFF
0xFFFE
S
T
R
I
N
G
Byte Addressable
memory for an
8-bit processor
with a 16-bit
addressing range
7
0
?
?
?
?
?
?
15
8
Bit
0x00000
0x00001
0xFFFFE
0xFFFFF
Byte Addressable
memory for a
16-bit processor
with a 20-bit
addressing range
Intel 80186
Little Endian
7
0
?
?
?
?
?
?
15
8
Bit
0x000001
0x000000
0xFFFFFF
0xFFFFFE
Byte Addressable
memory for a
16-bit processor
with a 24-bit
addressing range
MC68000
Big Endian
R2000 can post to either Big or Little Endian
Little
Big

## Slide 64: Memory Organization in 68K, x86, R2000, StrongARM
Bit
7
0
0x0000
0xFFFF
0xFFFE
S
T
R
I
N
G
Byte Addressable
memory for an
8-bit processor
with a 16-bit
addressing range
7
0
S
T
R
I
N
G
15
8
Bit
0x00000
0x00001
0xFFFFE
0xFFFFF
Byte Addressable
memory for a
16-bit processor
with a 20-bit
addressing range
Intel 80186
Little Endian
7
0
S
T
R
I
N
G
15
8
Bit
0x000001
0x000000
0xFFFFFF
0xFFFFFE
Byte Addressable
memory for a
16-bit processor
with a 24-bit
addressing range
MC68000
Big Endian
Little
Big